## Slide 1
Complex Numbers

## Slide 2
Introduction to Complex Numbers
A single frequency wave can be represented by a rotating vector called a phasor. Linear systems can alter this wave by scaling its amplitude and shifting its phase. Using complex numbers, this entire system transformation can be represented by a simple multiplication.
The Imaginary Unit, j
We define '' as an operator that rotates a phasor by () without changing its amplitude.
Multiplying by rotates a phasor by .
Multiplying by twice () rotates the phasor by π (), which is equivalent to multiplying by .
This leads to the fundamental definition of the imaginary unit: .

## Slide 3
Linear Systems and Phasors
A system is often represented as a box with an input and an output. We are interested in linear systems where a single-frequency wave input produces an output at the same frequency, but with a potentially different amplitude and phase.
Electrical Systems
Circuits made of resistors, capacitors, and inductors are a prime example. The input and output are typically voltages.
Mechanical Systems
Equivalent mechanical systems consist of masses, springs, and dampers. The input might be an external force and the output a displacement or tension.

## Slide 4
Representing Complex Numbers
Real and Imaginary Parts
A complex number, , is written as the sum of its real and imaginary parts: . In engineering, '' is used for the imaginary unit to avoid confusion with '' for current.
is the real part:
is the imaginary part:
The Complex Plane
Complex numbers are visualized on a 2D plane, often called an Argand diagram. The horizontal axis represents the real part, and the vertical axis represents the imaginary part.

## Slide 5
Basic Operations with Complex Numbers
Equality
Two complex numbers are equal only if their real parts are equal and their imaginary parts are equal.
If
then and
Addition
Add the real and imaginary parts separately.
This follows the parallelogram law for vectors.
Subtraction
Subtract the real and imaginary parts separately.
This is like adding the negative of the second vector.

## Slide 6
Multiplication and Conjugates
Multiplication
Multiply complex numbers in the same way as any algebraic expression, by expanding the brackets. Finally remember that
Example:
The Complex Conjugate
The conjugate of
Geometrically, it's a reflection across the real axis.
A number multiplied by its conjugate is always a real, non-negative number.
This value is also the square of the number's magnitude (modulus):

## Slide 7
Division of Complex Numbers
To divide complex numbers, we make the denominator a real number. This is done by multiplying both the numerator and the denominator by the complex conjugate of the denominator.
Example:
Step 1: Multiply top and bottom by the conjugate of the denominator
Fraction becomes:
Step 2: Expand the numerator and denominator.
Numerator:
Denominator:
Step 3: Simplify the result:

## Slide 8
Solving Quadratic Equations
Complex numbers provide a way to find solutions for any quadratic equation of the form
The Formula:
When b² - 4ac < 0, the term inside the square root is negative, which meant, when we only considered real numbers, there were no solutions.
With complex numbers, when we can write as
This means the solutions will be a pair of complex conjugates of the form
Therefore, if you know one complex root of a quadratic equation with real coefficients, the other root is simply its conjugate.

## Slide 9
Polar Form of a Complex Number
Instead of Cartesian coordinates , we can describe a complex number using its distance from the origin (modulus, r) and its angle from the positive real axis (argument, ). This is the polar form:
Cartesian to Polar
Modulus:
Argument: (with adjustment for the correct quadrant)
Polar to Cartesian
Real Part:
Imaginary Part:

## Slide 10
Operations in Polar Form
While addition and subtraction require conversion to Cartesian form, multiplication and division become much simpler in polar form.
Multiplication
To multiply, multiply the moduli and add the arguments.
(r₁∠θ₁) (r₂∠θ₂) = ()
Division
To divide, divide the moduli and subtract the arguments.
(r₁∠θ₁) / (r₂∠θ₂) = (r₁/r₂)∠(θ₁ - θ₂)

## Slide 11
Application: AC Circuit Analysis
Complex numbers are fundamental to analysing alternating current (AC) circuits. The relationship between voltage (), current (), and impedance () is a complex version of Ohm's Law:
Resistor
Impedance
It's a purely real value representing resistance.
Capacitor
Impedance
It's purely imaginary and called reactance. ω is the angular frequency.
Inductor
Impedance
It's also a purely imaginary reactance.

## Slide 12
Combining Impedances
Series Circuits
For components in series, the total impedance is the sum of the individual impedances.
Parallel Circuits
For parallel components.
or

## Slide 13
Circular Motion, Polar and Exponential Form
The Rotating Vector
A point moving in a circle with radius at a constant angular velocity can be described by:
z is a solution to the differential equation
which defines simple harmonic motion.
Exponential form
This shows the equivalence of the polar form of a complex number and the exponential form. Replacing by , it allows us to write any complex number in exponential form:
Where
We can show that is also a solution to the differential equation
with the same initial conditions:and velocity , at
So,

## Slide 14
1
2
3
The Exponential Form
The exponential form z = r e jθ simplifies complex number operations as we can use the standard rules of exponents.
Multiplication
Division
Powers
This can be used to show De Moivre’s theorem
So
=

## Slide 15
Trigonometric and Hyperbolic Functions
Trigonometric Expressions
Link to Hyperbolic Functions
Using e jθ = cos(θ) + j sin(θ) we can find expressions linking trigonometric and hyperbolic functions.

## Slide 16
Solving Equations: The Roots of Unity
The exponential form is invaluable for finding the -th roots of a complex number, such as solving the equation , known as finding the '-th roots of unity'.
The Method
Write the number in its general exponential form, acknowledging that angles repeat every . For 1, this is , where N is an integer.
The equation becomes
Take the -th root of both sides:
Let to find the n distinct roots.
The Result
The n roots are always evenly spaced around a circle in the complex plane, e.g. the 5th roots of unity below.

## Slide 17
Summary
Complex Numbers
Cartesian form:
Polar form:
Exponential form:
Operations
Add/Subtract in Cartesian
Multiply/Divide in Polar/Exponential
Use conjugate for division
Applications
Solving quadratics
AC circuit analysis ()
Describing circular motion & waves
Key Formulas
Euler’s formula:
De Moivre's Theorem:
Powers: